## Slide 1
5-2 ANALOG AND DIGITAL
Analog-to-analog conversion is the representation of analog information by an analog signal. One may ask why we need to modulate an analog signal; it is already analog. Modulation is needed if the medium is bandpass in nature or if only a bandpass channel is available to us.
Amplitude Modulation
Frequency Modulation
Phase Modulation
Topics discussed in this section:

## Slide 2
Figure 5.15 Types of analog-to-analog modulation

## Slide 3: Amplitude Modulation
A carrier signal is modulated only in amplitude value
The modulating signal is the envelope of the carrier
The required bandwidth is 2B, where B is the bandwidth of the modulating signal
Since on both sides of the carrier freq. fc, the spectrum is identical, we can discard one half, thus requiring a smaller bandwidth for transmission.

## Slide 4
Figure 5.16 Amplitude modulation

## Slide 5
The total bandwidth required for AM can be determined
from the bandwidth of the audio signal: BAM = 2B.
Note

## Slide 6
Figure 5.17 AM band allocation

## Slide 7: Frequency Modulation
The modulating signal changes the freq. fc of the carrier signal
The bandwidth for FM is high
It is approx. 10x the signal frequency

## Slide 8
Figure 5.18 Frequency modulation

## Slide 9
The total bandwidth required for FM can be determined from the bandwidth of the audio signal: BFM = 2(1 + β)B. Where  is usually 4.
Note

## Slide 10
Figure 5.19 FM band allocation

## Slide 11: Phase Modulation (PM)
The modulating signal only changes the phase of the carrier signal.
The phase change manifests itself as a frequency change but the instantaneous frequency change is proportional to the derivative of the amplitude.
The bandwidth is higher than for AM.

## Slide 12
Figure 5.20 Phase modulation

## Slide 13
The total bandwidth required for PM can be determined from the bandwidth and maximum amplitude of the modulating signal: BPM = 2(1 + β)B.
Where  = 2 most often.
Note