## Slide 1
Bandwidth Utilization:
Multiplexing

## Slide 2
Bandwidth utilization is the wise use of available bandwidth to achieve specific goals.
Efficiency can be achieved by multiplexing; i.e., sharing of the bandwidth between multiple users.
Note

## Slide 3
6-1 MULTIPLEXING
Whenever the bandwidth of a medium linking two devices is greater than the bandwidth needs of the devices, the link can be shared. Multiplexing is the set of techniques that allows the (simultaneous) transmission of multiple signals across a single data link. As data and telecommunications use increases, so does traffic.
Frequency-Division Multiplexing
Wavelength-Division Multiplexing
Synchronous Time-Division Multiplexing
Statistical Time-Division Multiplexing
Topics discussed in this section:

## Slide 4
Figure 6.1 Dividing a link into channels

## Slide 5
Figure 6.2 Categories of multiplexing

## Slide 6
Figure 6.3 Frequency-division multiplexing (FDM)

## Slide 7
FDM is an analog multiplexing technique that combines analog signals.
It uses the concept of modulation discussed in Ch 5.
Note

## Slide 8
Figure 6.4 FDM process

## Slide 9: FM

## Slide 10
Figure 6.5 FDM demultiplexing example

## Slide 11
Assume that a voice channel occupies a bandwidth of 4 kHz. We need to combine three voice channels into a link with a bandwidth of 12 kHz, from 20 to 32 kHz. Show the configuration, using the frequency domain. Assume there are no guard bands.
Solution
We shift (modulate) each of the three voice channels to a different bandwidth, as shown in Figure 6.6. We use the 20- to 24-kHz bandwidth for the first channel, the 24- to 28-kHz bandwidth for the second channel, and the 28- to 32-kHz bandwidth for the third one. Then we combine them as shown in Figure 6.6.
Example 6.1

## Slide 12
Figure 6.6 Example 6.1

## Slide 13
Five channels, each with a 100-kHz bandwidth, are to be multiplexed together. What is the minimum bandwidth of the link if there is a need for a guard band of 10 kHz between the channels to prevent interference?
Solution
For five channels, we need at least four guard bands. This means that the required bandwidth is at least
5 × 100 + 4 × 10 = 540 kHz,
as shown in Figure 6.7.
Example 6.2

## Slide 14
Figure 6.7 Example 6.2

## Slide 15
Four data channels (digital), each transmitting at 1 Mbps, use a satellite channel of 1 MHz. Design an appropriate configuration, using FDM.
Solution
The satellite channel is analog. We divide it into four channels, each channel having 1M/4=250-kHz bandwidth.
Each digital channel of 1 Mbps must be transmitted over a 250KHz channel. Assuming no noise we can use Nyquist to get:
C = 1Mbps = 2x250K x log2 L -> L = 4 or n = 2 bits/signal element.
One solution is 4-QAM modulation. In Figure 6.8 we show a possible configuration with L = 16.
Example 6.3

## Slide 16
Figure 6.8 Example 6.3

## Slide 17
Figure 6.9 Analog hierarchy

## Slide 18
The Advanced Mobile Phone System (AMPS) uses two bands. The first band of 824 to 849 MHz is used for sending, and 869 to 894 MHz is used for receiving. Each user has a bandwidth of 30 kHz in each direction. How many people can use their cellular phones simultaneously?
Solution
Each band is 25 MHz. If we divide 25 MHz by 30 kHz, we get 833.33. In reality, the band is divided into 832 channels. Of these, 42 channels are used for control, which means only 790 channels are available for cellular phone users.
Example 6.4

## Slide 19
Figure 6.10 Wavelength-division multiplexing (WDM)

## Slide 20
WDM is an analog multiplexing technique to combine optical signals.
Note

## Slide 21
Figure 6.11 Prisms in wavelength-division multiplexing and demultiplexing

## Slide 22
Figure 6.12 Time Division Multiplexing (TDM)

## Slide 23
TDM is a digital multiplexing technique for combining several low-rate digital channels into one high-rate one.
Note

## Slide 24
Figure 6.13 Synchronous time-division multiplexing

## Slide 25
In synchronous TDM, the data rate of the link is n times faster, and the unit duration is n times shorter.
Note

## Slide 26
In Figure 6.13, the data rate for each one of the 3 input connection is 1 kbps. If 1 bit at a time is multiplexed (a unit is 1 bit), what is the duration of (a) each input slot, (b) each output slot, and (c) each frame?
Solution
We can answer the questions as follows:
a. The data rate of each input connection is 1 kbps. This means that the bit duration is 1/1000 s or 1 ms. The duration of the input time slot is 1 ms (same as bit duration).
Example 6.5

## Slide 27
b. The duration of each output time slot is one-third of the input time slot. This means that the duration of the output time slot is 1/3 ms.
c. Each frame carries three output time slots. So the duration of a frame is 3 × 1/3 ms, or 1 ms.
Note: The duration of a frame is the same as the duration of an input unit.
Example 6.5 (continued)

## Slide 28
Figure 6.14 shows synchronous TDM with 4 1Mbps data stream inputs and one data stream for the output. The unit of data is 1 bit. Find (a) the input bit duration, (b) the output bit duration, (c) the output bit rate, and (d) the output frame rate.
Solution
We can answer the questions as follows:
a. The input bit duration is the inverse of the bit rate: 1/1 Mbps = 1 μs.
b. The output bit duration is one-fourth of the input bit duration, or ¼ μs.
Example 6.6

## Slide 29
Figure 6.14 Example 6.6

## Slide 30
c. The output bit rate is the inverse of the output bit duration 4 Mbps. This can also be deduced from the fact that the output rate is 4 times as fast as any input rate; so the output rate = 4 × 1 Mbps = 4 Mbps.
d. The frame rate is always the same as any input rate. So the frame rate is 1,000,000 frames per second. Because we are sending 4 bits in each frame, we can verify the result of the previous question by multiplying the frame rate by the number of bits per frame.
Example 6.6 (continued)

## Slide 31
Four 1-kbps connections are multiplexed together. A unit is 1 bit. Find (a) the duration of 1 bit before multiplexing, (b) the transmission rate of the link, (c) the duration of a time slot, and (d) the duration of a frame.
Solution
We can answer the questions as follows:
a. The duration of 1 bit before multiplexing is 1 / 1 kbps, or 0.001 s (1 ms).
b. The rate of the link is 4 times the rate of a connection, or 4 kbps.
Example 6.7

## Slide 32
c. The duration of each time slot is one-fourth of the duration of each bit before multiplexing, or 1/4 ms or 250 μs. Note that we can also calculate this from the data rate of the link, 4 kbps. The bit duration is the inverse of the data rate, or 1/4 kbps or 250 μs.
d. The duration of a frame is always the same as the duration of a unit before multiplexing, or 1 ms. We can also calculate this in another way. Each frame in this case has four time slots. So the duration of a frame is 4 times 250 μs, or 1 ms.
Example 6.7 (continued)

## Slide 33: Interleaving
The process of taking a group of bits from each input line for multiplexing is called interleaving.
We interleave bits (1 - n) from each input onto one output.

## Slide 34
Figure 6.15 Interleaving

## Slide 35
Four channels are multiplexed using TDM. If each channel sends 100 bytes /s and we multiplex 1 byte per channel, show the frame traveling on the link, the size of the frame, the duration of a frame, the frame rate, and the bit rate for the link.
Solution
The multiplexer is shown in Figure 6.16. Each frame carries 1 byte from each channel; the size of each frame, therefore, is 4 bytes, or 32 bits. Because each channel is sending 100 bytes/s and a frame carries 1 byte from each channel, the frame rate must be 100 frames per second. The bit rate is 100 × 32, or 3200 bps.
Example 6.8

## Slide 36
Figure 6.16 Example 6.8

## Slide 37
A multiplexer combines four 100-kbps channels using a time slot of 2 bits. Show the output with four arbitrary inputs. What is the frame rate? What is the frame duration? What is the bit rate? What is the bit duration?
Solution
Figure 6.17 shows the output (4x100kbps) for four arbitrary inputs. The link carries 400K/(2x4)=50,000 2x4=8bit frames per second. The frame duration is therefore 1/50,000 s or 20 μs. The bit duration on the output link is 1/400,000 s, or 2.5 μs.
Example 6.9

## Slide 38
Figure 6.17 Example 6.9

## Slide 39: Data Rate Management
Not all input links maybe have the same data rate.
Some links maybe slower. There maybe several different input link speeds
There are three strategies that can be used to overcome the data rate mismatch: multilevel, multislot and pulse stuffing

## Slide 40: Data rate matching
Multilevel: used when the data rate of the input links are multiples of each other.
Multislot: used when there is a GCD between the data rates. The higher bit rate channels are allocated more slots per frame, and the output frame rate is a multiple of each input link.
Pulse Stuffing: used when there is no GCD between the links. The slowest speed link will be brought up to the speed of the other links by bit insertion, this is called pulse stuffing.

## Slide 41
Figure 6.19 Multilevel multiplexing

## Slide 42
Figure 6.20 Multiple-slot multiplexing

## Slide 43
Figure 6.21 Pulse stuffing

## Slide 44: Synchronization
To ensure that the receiver correctly reads the incoming bits, i.e., knows the incoming bit boundaries to interpret a “1” and a “0”, a known bit pattern is used between the frames.
The receiver looks for the anticipated bit and starts counting bits till the end of the frame.
Then it starts over again with the reception of another known bit.
These bits (or bit patterns) are called synchronization bit(s).
They are part of the overhead of transmission.

## Slide 45
Figure 6.22 Framing bits

## Slide 46
We have four sources, each creating 250 8-bit characters per second. If the interleaved unit is a character and 1 synchronizing bit is added to each frame, find (a) the data rate of each source, (b) the duration of each character in each source, (c) the frame rate, (d) the duration of each frame, (e) the number of bits in each frame, and (f) the data rate of the link.
Solution
We can answer the questions as follows:
a. The data rate of each source is 250 × 8 = 2000 bps = 2 kbps.
Example 6.10

## Slide 47
b. Each source sends 250 characters per second; therefore, the duration of a character is 1/250 s, or 4 ms.
c. Each frame has one character from each source, which means the link needs to send 250 frames per second to keep the transmission rate of each source.
d. The duration of each frame is 1/250 s, or 4 ms. Note that the duration of each frame is the same as the duration of each character coming from each source.
e. Each frame carries 4 characters and 1 extra synchronizing bit. This means that each frame is 4 × 8 + 1 = 33 bits.
Example 6.10 (continued)

## Slide 48
Two channels, one with a bit rate of 100 kbps and another with a bit rate of 200 kbps, are to be multiplexed. How this can be achieved? What is the frame rate? What is the frame duration? What is the bit rate of the link?
Solution
We can allocate one slot to the first channel and two slots to the second channel. Each frame carries 3 bits. The frame rate is 100,000 frames per second because it carries 1 bit from the first channel. The bit rate is 100,000 frames/s × 3 bits per frame, or 300 kbps.
Example 6.11

## Slide 49
Figure 6.23 Digital hierarchy

## Slide 50
Table 6.1 DS and T line rates

## Slide 51
Figure 6.24 T-1 line for multiplexing telephone lines

## Slide 52
Figure 6.25 T-1 frame structure

## Slide 53
Figure 6.26 TDM slot comparison